Electronics     Ph. D. Qualification Examination 2011               07/20/201

Name:                                         ID#:

- (5%) Please derive the Vo/Vi of the following circuit?

- (10%) Consider the difference amplifier in the following ficture with two input terminals connected together to an input common-mode signal source. For R2/R1= R4/ R3, show that the input common-mode resistance is .

- (5%) What are the output waveforms of following diode circuits?

Ans:

- (15%) For the circuits in the following picture, (nCox=2.5 (pCox=20(A/V2,  , (=0,  (=0, L=10(m, and W=30(m, unless otherwise specified. Find the labeled currents and voltages

Ans:

5. (10%) The circuit in the following figure provides a constant current IO as long as the circuit to which the collector is connected maintains the BJT in the active mode. Show that

Ans:

6. (10%)  In the circuit shown in the following figure, measurement indicates VB to be +1.0V, VE to be +1.7V. What are ( and ( for this transistor? What voltage VC do you expect at the collector?

Ans:

7. (15%)  vsig is a small sinewave signal with zero average. (=100.

(a) Find RE to establish a dc emitter current of about 0.5mA.

(b) Find RC to establish a dc collector voltage of about 5V.

(c) RC =10k( and ro=200k(, draw the small signal equivalent circuit of the amplifier and determine the overall voltage gain vo/vsig.

Ans:

- (10%) Please find the unit gain bandwidth in the following figure.

Ans:

- (5%) Find the Io of the following current mirror.

Ans:

- (10%) Find the input resistance of common gate amplifier.

Ans:

- (5%) What is the function of the following figure?

Ans: